## Slide 1: UG WorkPlan Job

## Slide 2: UG Subdivision
UG subdivision jobs require detail planning and intricate design. Today we will show you processes that will make designing subdivision more time efficient while creating an accurate and easy to read drawing.
We will begin staking in a newly designed subdivision that features no existing power.

## Slide 3: UG Subdivision
When designing a subdivision location of lines is extremely important. Parcels and easements are already in place and we need to make sure we stay within our designated area while also providing a clear and accurate drawing. To achieve this we will focus on using the “Create Offset Locations” tool.

## Slide 4: UG Subdivision – Select Features
We start by selecting the feature that we will offset from, in this case it will be roads (centerline).
Once the parcels are selected we w will be able to use the “Draw Offset” tool to draw our line an exact distance from the selected feature.

## Slide 5: UG Sudivision: Creating Offset Locations
If you’re walking in the direction that you intend to draw.
A positive number will offset the line to the right hand side of your selected feature.
A negative number will offset the line to the left hand side of your selected feature.

## Slide 6: UG Subdivision – Open Points
Another important part of subdivison design is Open Points. Open Points give the designer the flexibility to feed the subdivision form different sources based on load or in the event of an outage.
By creating a location just short of the cabinet we will be able to stake an Open Point.

## Slide 7: UG Subdivision: Open Points
Once the second conductor has been swung to the cabinet set Enabled to “False” in the fields tab of the conductor.
Setting Enabled to “False” will prevent flow from being set through the short span during posting. This allows the designer to show the Open Points accurately for crew building the job.
Once the job is posted the Mapper can use the Open Point feature tool to place the actual Open Point and symbolize it based on their in house standards.

## Slide 8: UG Subdivision
In closing we are using the “Create Offset Locations” tool to lay out the 3-phase feeds and single phase taps through the subdivision and creating our Open Points and backfeeds as need.
Once all of the conductor is in place on the drawing the staker can place pad transformers and any other underground construction units in the pallete and use the “Add OH Locations” tool to place transformer locations where they are needed.

## Slide 9: TITLE GOES HERE
Click to add text
Click to add text